## Slide 1: Privacy and security Implications on Wireless (Wi-Fi)
J R O Sirimanne
2013 MIS 021

## Slide 2: Road Map
Introduction
Background
Design of the research
Research findings so far…

## Slide 3: Introduction
Wi-Fi is the popular wireless networking technology using radio waves operate in 2.4GHz and 5GHz bands
a huge growth in Wi-Fi enabled devices and Wi-Fi hotspots within past few years
Tomography refers to imaging by sections or sectioning, through the use of any kind of penetrating wave
Radio tomographic imaging (RTI) offers a new way to image passive objects in buildings and outdoor environments using received signal strength (RSS).
Signal Strength is measured in decibel (db)
RSSI is a measurement of the power present in a received radio signal

## Slide 4: Privacy
freedom from interference or intrusion
the right "to be let alone,“
Privacy and tomography???
  In tomography it is possible to map objects
  Objects can be anything including “HUMANS”
  No way to know whether someone is using tomographic technologies
“Human movements can be mapped even without their knowledge” !!!
Privacy is breached

## Slide 5: Related Work
RADAR: An In-Building RF-based User Location and Tracking System by Paramvir Bahl and Venkata N. Padmanabhan IEEE Infocom 2000, volume 2, pages 775-784, March 2000.
  An In-building RF-based user location and tracking system
  WiFi-based localization
  Fingerprinting, RSSI profiling

## Slide 6: Related Work Contd…
J. Wilson and N. Patwari, “Radio tomographic imaging with wireless networks,” IEEE Transactions on Mobile Computing, vol. 9, no. 5, pp. 621–632, May 2010. Published, 01/08/2010.
tracks humans moving through a building
An illustration of an Radio tomographic imaging (RTI) network. Each node broadcasts to the others, creating many projections that can be used to reconstruct an image of objects inside the network area.

## Slide 7: Related Work Contd…
Study on wireless sensor based industrial tomography systems by Chiew Loon Goh, Nor Muzakir Nor Ayob, Ruzairi Abdul Rahim, Herlina Abdul Rahim, Muhammad Jaysuman Pusppanathan, Mohd. Hafiz Fazalul Rahiman, Leow Pei Ling, Zulkarnay Zakaria.
  survey on wireless based industrial tomography system, and to review design challenges in the field of embedded wireless solutions

## Slide 8: Related Work - Products

## Slide 9: Research Question
Is there a significant amount of wireless signal strength drop when there is a human inside the line of sight of the wireless access point and data gathering computer?
How accurately we can identify human presence by observing received signal strength indicator (RSSI) values.

## Slide 10: Design
Creating initial scenario sets to gather data
Developed to answer first research question
Try to make them as close as possible to real world situations
Two variables
  Wireless access point
  Data gathering computer
At any given time one is constant

## Slide 11: Scenarios – Set 1
When Wireless access points position is a constant and its in the middle of the room
  Wireless access point Data gathering computer
Scenario 1 Scenario 2 Scenario 3
Scenario 4 Scenario 5 Scenario 6

## Slide 12: Scenarios – Set 1 Contd…
When Wireless access points position is a constant and its in the middle of the room
  Wireless access point Data gathering computer
Scenario 7 Scenario 8

## Slide 13: Scenarios – Set 2
When Wireless access points position is a constant and its in a corner of the room
  Wireless access point Data gathering computer
Scenario 9 Scenario 10 Scenario 11
Scenario 12

## Slide 14: Scenarios – Set 3
When Wireless access points position is a constant and its in a middle corner of the room
  Wireless access point Data gathering computer
Scenario 13 Scenario 14 Scenario 15
Scenario 16

## Slide 15: Scenarios – Set 4
From above scenarios we randomly select scenario 12 and place a human between Wireless access point and Data gathering computer
  Wireless access point Data gathering computer
  Human
Here position of Wireless access point and Data gathering computer is constant and human position is the variable
Scenario 12-1 Scenario 12-2 Scenario 12-3

## Slide 16: Gathering Data
Received Signal Strength is gathered from scenarios mentioned earlier.
Using a python script
  http://recolog.blogspot.com/2015/03/plotting-wifi-signal-strength-variation.html
15 minutes of Received Signal Strength Data
Approximately 6 samples per second (value every 0.333 ms)
Received Signal Strength Data is saved to a text file
Laptop
Wireless Access Point

## Slide 17: Analyzing Data
Plot signal strength values in a graph for scenario 1
Draw normal distribution graphs for each scenario
  X axis = Signal Strength in db
  Y axis = Density of probability (the chance of obtaining values near corresponding points on the X-axis)

## Slide 18: Normal Distribution Graphs Set 1
Chart: SC1
Chart: SC2
Chart: SC3
Chart: SC4

## Slide 19: Normal Distribution Graphs Set 1 Contd…
Chart: SC5
Chart: SC6
Chart: SC7
Chart: SC8

## Slide 20: Normal Distribution Graphs Set 2
Chart: SC9
Chart: SC10
Chart: SC11
Chart: SC12

## Slide 21: Normal Distribution Graphs Set 3
Chart: SC13
Chart: SC14
Chart: SC15
Chart: SC16

## Slide 22: Normal Distribution Graphs Set 4
Chart: SC12.1
Chart: SC12.2
Chart: SC12.3

## Slide 23: Answering Research Question
Answer first research question we use a statistical approach
statistical hypothesis testing
is an assumption about a population parameter. This assumption may or may not be true. Hypothesis testing refers to the formal procedures used by statisticians to accept or reject statistical hypotheses.
Building the hypothesis
  Null hypothesis – H0 = there is no change to amount of wireless signal strength when there is a human and no human inside the line of sight of the wireless access point and data gathering computer
  Alternative hypothesis – H1 = there is a significant amount of wireless signal strength drop when there is a human inside the line of sight of the wireless access point and data gathering computer

## Slide 24: Answering Research Question..
Proving the hypothesis with regard to scenario 12
  Using a 0.05 level of significance
  Calculate values
Scenario | Mean | T-Test value

## Slide 25: Questions?

## Slide 26: Thank You!